## Slide 1
EMBEDDED SYSTEMS PROJECT
Smart Fridge
Door Monitor
IoT-Based Access Tracking via Rotary Encoder & Telegram Bot
Meshal Mohammed 223048650 · Omar Alhamed 222406431 · Yousef Alhashim 223038205 · Yazeed Almuslim 222449093
Supervised by Dr. Ramasamy | April 2026
KFU · CCSIT

## Slide 2
Table of Contents
01 Problem Statement
Gap Analysis & Our Solution
02 System Architecture
Sensing, Processing & UI Units
03 Hardware Design
Components & Pin Connections
04 Software Design
Shelf & User Detection Algorithms
05 Results & Discussion
Person ID & Shelf Detection Results
06 Conclusion
Key Achievements & Future Work

## Slide 3
Problem Statement
The Gap
Ordinary fridges have no usage tracking
No record of who opened the door or when
No alerts when door is left open
Leads to energy waste & food expiration
No real-time family notifications
Our Solution
Low-cost, non-intrusive IoT monitor
Rotary encoder tracks door angle (0–9)
Identifies shelf/drawer accessed
Identifies user by opening speed
Instant Telegram bot notifications
LED + alert if door open > 30 seconds

## Slide 4
System Architecture
1. Sensing Unit
KY-040 Rotary Encoder
Mounted on fridge hinge
CLK, DT, SW signals
Tracks door angle (0–9 positions)
Button simulates door close
2. Processing & Connectivity
ESP32-WROOM-32 MCU
Reads encoder signals
Calculates position, speed,
open duration
Connects via home Wi-Fi
Sends data to Telegram Bot
3. User Interface
Telegram Bot (smartphone)
Onboard LED (GPIO 2)
Flashes if door open >30s
Serial Monitor (USB debug)
Event log with user & shelf

## Slide 5
Hardware Design
Components
ESP32-WROOM-32 development board
KY-040 Rotary Encoder (with push button)
Onboard LED (GPIO 2)
5V USB power supply
Jumper wires & Breadboard
Pin Connections
Component | ESP32 GPIO
Encoder CLK | GPIO 23
Encoder DT | GPIO 25
Encoder SW (Btn) | GPIO 26
Onboard LED | GPIO 2
The encoder shaft is attached to the fridge hinge — rotating the door rotates the encoder.

## Slide 6
Software Design
Shelf Detection Algorithm
Maps max door position to fridge shelf:
Max Position | Shelf / Area
0 – 1 | Door closed / just opened
2 – 3 | Left door rack (front)
4 – 5 | Right door rack
6 – 7 | Middle shelf
8 – 9 | Deep shelf / crisper drawer
Person Identification Algorithm
Speed = (maxPosition × 1000) / timeToMax
User | Speed (pos/s) | Category
Father | > 3.67 | Fast
Me | 2.34 – 3.67 | Medium
Mom | 1.00 – 2.33 | Slow
Kid | < 1.00 | Very Slow
Thresholds determined experimentally by recording each
family member's opening speed across multiple trials.

## Slide 7
Results & Discussion
Person Identification Results
Member | Avg Speed | Accuracy
Father | 4.50 pos/s | 100%
Me | 3.20 pos/s | 95%
Mom | 1.75 pos/s | 92%
Kid | 0.80 pos/s | 100%
All 4 users identified with ≥ 92% accuracy
Tested across multiple opening distances and sessions.
Shelf Detection Results
Max Pos | Item Taken | Reported
2 | Butter | Left door rack ✓
4 | Juice | Right door rack ✓
6 | Leftover container | Middle shelf ✓
8 | Carrots (crisper) | Deep shelf ✓
100% shelf detection accuracy in all test cases
Telegram notification delivered within 2 seconds.
LED blinks + alert after 30s door-open (no spam).

## Slide 8
CONCLUSION
Key Achievements
✔
Low-cost, plug-and-play fridge monitoring system
✔
Door position tracked via rotary encoder (0–9 scale)
✔
Shelf/drawer access identified with 100% accuracy
✔
User identification by opening speed — ≥ 92% accuracy
✔
Real-time Telegram notifications within 2 seconds
✔
LED warning + alert message after 30-second open
Future Work: Mobile app integration · Temperature sensors · Cloud dashboard